Computer buses
Introduction
As an introduction to PCI Express bus, we will start talking about the theoretical and general shared bus structure in the PC style computer. We will follow this with a discussion of bus communication protocols. After that we will be ready to understand exactly how bus arbitration works. And Finally we will be focused on Peripheral Component Interconnect expresses (PCIe) device and its routing capability ties.
Shared bus structure
Bus technology connects components of computer system and is used to transport data between them. Aside from actual data, buses not only provides signaling information to ensure that data has reached its destination, but also provides for signaling flow control of data to ensure that the devices are ready to send or accept data when necessary. Flow control also defines at which speed two devices will communicate with each other. The bus consists of components that are connected by wires, and which usually appear as tracks on a Printed Circuit Board (PCB).
There are four types of buses: address, power, control, and data. Buses consists of a number of parallel lines that are connected between the memory, CPU and I/O devices. The information on the address bus allows memory and I/O devices to be accessed (by their address). The data bus , also, consists of parallel lines. Data buses are used to send data and instructions. Control buses are a collection of lines designated for tasks such as request, write, read and reset. Power buses provide basic power to devices.
Speed of data transfer
Buses can be built in two modes: serial and parallel. In serial mode, data is transferred one bit at a time. In parallel mode data is sent multiple bits at a time. For example, if an 8-bit character is sent using serial mode, it will be sent bit by bit. But in parallel mode, 8 bits are sent simultaneously at a time through 8 separate wires. Parallel mode has some some problems that must be overcome. When an electric current is sent through the wire, it is creating the electromagnetic field that may influence the adjacent electric currents. In this case, the receiving device may get incorrect data. This is called Electromagnetic Interference (EMI). Wires on a motherboard, being imperfect, are not always the same size. When a bit is sent through the shorter wire, it will get to destination faster than other bits sent in a parallel set. This results the receiving device having to wait until all bits are arrive, which causes issue called propagation delay.
Data on a bus can be sent at burst or sustained rate. The burst rate is a maximum rate at which data can be sent over a bus. The sustained rate is a rate at which data can be sent over a bus in a constant manner. To understand these rates, let’s look at the analogy of the sprint runner and the long distance runner. A sprint runner can run with a very high speed in a short time, but he cannot maintain his speed. Long distance runner maintains his constant speed to reach a specific location. This example reflects the key difference between these two rates and this concept applies to buses. The sustained rate is better metric, because it reflects the typical transmission speed.

Shared bus protocols
A protocol is a set of rules agreed upon by buses as to how information is to be sent over the bus. One of the main functions of bus protocol is Flow control. Suppose that two computers are communicating with each other for uploading or downloading data. At some point, one of the computers will need to store the received information on a disk. But what happens if computer is receiving data while writing file on a disk? That’s where flow control plays its role.
Flow control allows the receiving device to regulate the flow of data sent by the sending device. Some protocols allow two communicating devices to agree upon the size of block to be sent to each other. A block is a portion of the data which the protocol defines. The data is divided into packages of a specific size, a defined block. These blocks are usually either of 128, 256, 512, 1024, or 2048 Kbytes in size. Mechanisms exists to ensure that the data received by the receiving device is correct. The sending device performs calculations on the block that it is will send. This might be 1 to 2 bytes called a Block Check Character (BCC). When the receiving device receives the block, it also starts to calculate BCC of the data in the block. The receiving device compares the value of BCC, both which it computed and that which it received. If they are equal, then the receiving device informs the sending device that everything is alright. If BCC values are not equal, the receiving device asks the sending device to resend the block. The sending device transmits only one block at a time.
Bus protocols can be open or proprietary. In order to connect a device to a bus, for example, the PCI bus (which we will cover later), the device, and the software which runs it, must be implemented with PCI bus protocol to the letter. The main reason of having different standards are business strategies. Usually the most successful bus protocols are open standards, which PCI is. Manufacturers are not obliged to pay money to the developer for implementing PCI into the devices that they are creating. This allows different manufacturers to compete with other manufacturers while ensuring the buyer that their product will be working on every computer that includes a PCI bus.
Buses can operate using synchronous, asynchronous or semi-synchronous communication protocols. A device that starts a read or write operation is called the master device. A device that the master device communicates with is called a slave device. If, for example, CPU requests data from memory (Read operation), then the CPU is a master device and the memory is a slave device.
Asynchronous bus devices are not supposed to send or receive data at the fixed clock rate. Additional handshake lines will be needed to guarantee that information is sent or received. This mode can achieve the maximum throughput between devices and allows the slow and fast devices to communicate with each other. Asynchronous protocols use two control signals: MSYNC (Master sync signal) – which is sent by a master device, indicating that it is ready and SSYNC (Slave sync signal) – which is sent by slave device, indicating that it is ready.

Let’s look at the steps of the CPU (master) reading data from memory (slave) using asynchronous protocol:
1) CPU sends address information and asserts MREQ and READ. Address information indicates where exactly the required information is located in memory. Asserting MREQ (memory request) and READ indicates that CPU requests information from memory;
2) CPU asserts MSYNC. The most important thing to remember here is that MSYNC must be asserted after asserting the triplet of MREQ, READ and sending address information. The MSYNC signal states that the currently asserted MREQ, READ and sent address information are correct;
3) CPU waits for the SSYNC signal response from memory;
4) After receiving SSYNC signal from memory, CPU copies the received data into MBR (Memory Buffer Register);
5) CPU removes MSYNC request. Again, MSYNC must be removed before removing MREQ and READ requests due to the same reasons mentioned before;
6) CPU removes address information, MREQ and READ requests.
Figure 1 illustrates the example of asynchronous protocol:

Synchronous bus devices communicate with each other at a fixed clock rate. This clock dictates when exactly the data will arrive in a certain time range. If a device hasn’t received data in certain clock time, data is lost. Synchronous transfer occurs in register-to-register transfer within the CPU. Let’s look at the steps of the CPU reading data from memory using synchronous protocol:
1) At rise of a clock, CPU sends address information;
2) At fall of a clock, CPU asserts MREQ and READ to request data from memory;
3) At fall of next clock, memory is ready to send the data to the CPU. After copying data into MBR, CPU removes address information, MREQ and READ.

Figure 2 illustrates the example of synchronous protocol:

The WAIT signal informs CPU that it should wait before the data from memory is ready. It is expected that some event is going at occur at a rise/fall of the bus clock, but these events do not occur immediately due to physics: some time is required for clock signal to travel from bus to CPU. In the Figure 2, these delays are marked as:
TAD – Delay between rise of a clock and sending address information;
TMD – Delay between fall of a clock and asserting MREQ;
TRD – Delay between fall of a clock and asserting READ.
Semi-synchronous mode combines benefits of synchronous and asynchronous modes. It has the speed of synchronous bus and allows different slow and fast devices to communicate with each other. In semi-synchronous mode the communication between master and slave is still regulated by fixed clock rate, but if a slave is not be able to provide data to the master in the required time, it will be allowed to send data during several clock cycles. Example of semi-synchronous communication is between CPU and Main memory.
There are two types of buses: Dedicated and Multiplexed. Dedicated bus has only one function (address or data). Multiplexed buses consist of lines that act like an address bus or data bus in a shared period of time. This means that in one period the bus transfers address information and in another period bus transfers data information. This type of a bus was used in earlier microcomputers and is cheaper than dedicated bus, but it is slower. Modern high performance computers use dedicated buses.
A bus cannot be used by several devices at the same time. This is because of the electrical properties of the devices (it can cause damage). A solution for this is arbitration: devices get permission before sending information. Bus arbitration and bus utilization always happen at the same time. While the bus is currently being used, other devices which are competing for bus access elect which one of them is going to use the bus next time.

 There are two types of arbitration: Centralized and Distributed. In centralized arbitration there is only one master which gives permission to slave devices. Let’s look at centralized arbiter of PCI bus:

PCI’s centralized arbitration depends on the priority of slave devices. In this case, a device with the highest number has highest priority. By looking at the Table 1, you may notice that PCI Dev 2 always has the highest priority comparing to other devices. If the value of ReqX (X=0,1,2) equals to 1, then PCI Dev X (X=0,1,2) sends request for the bus usage. Otherwise, if ReqX equals to 0, then the device is idle. If GrantX equals to 1, PCI Arbiter grants PCI Dev X permission for using the bus.
Req2	Req1	Req0	Grant2	Grant1	Grant0
0	0	0	0	0	0
0	0	1	0	0	1
0	1	0	0	1	0
0	1	1	0	1	0
1	0	0	1	0	0
1	0	1	1	0	0
1	1	0	1	0	0
1	1	1	1	0	0

In distributed arbitration, there is no central controller. In this case, control logic is on every device. Figure 5 illustrates this scenario:

Bus Types and Standards
PCI (Peripheral Component Interconnect) is a 32 bit synchronous bus with multiplexed address and data lines that can run at up to 33Mhz clock rate. This bus transfers data in parallel mode.
 AGP (Accelerated Graphics Port) is a bus for video cards which also transfer data in parallel mode. AGP was a successor to the PCI bus. Over the time, video adapters have evolved and became bandwith-hungry. PCI’s shared bus architecture constrained the devices from operating at full speed. AGP is using point-to-point architecture which allows direct communication with CPU without sharing a bus. It also uses dedicated data and address lines so the entire packet does not need to be read to get the address. Graphic adapters use a separate 8-bit “SideBand address” bus to send AGP request and command information while using 32 data/address lines to send AGP data at the same time. The other advantage is that for loading textures, AGP graphic card can directly read textures from the main memory whereas PCI graphic card must first copy these textures from main memory to card’s video memory and then read them.
PCIe (Peripheral Component Interconnect express)
A better version of PCI bus was invented with the name of PCIe (Peripheral Component Interconnect express). Currently this is the most popular bus used in contemporary computer systems, which replaced the older PCI, PCI-X and AGP buses. PCIe transfers data in serial mode.
PCIe is implemented using the point-to-point topology. PCIe devices communicate with each other using a packet based communications protocol, which is similar to the TCP/IP protocols used in the computer networks. It is available in a variety of different physical configuration, such as x1, x4, x8, x16, x32 and it is upward and downward compatible. The PCIe x4 card can be fit into every single PCIe slot (x1, x4, x8, x16), but if PCIe card’s configuration is lower than the PCIe slot’s, it will have less bandwith. In case of x1 slot, PCIe x4 card’s bandwith will be limited to PCIe x1 slot’s bandwith. In case of x16 slot, PCIe x4 card’s bandwith won’t be limited, but it still won’t be able to have more bandwith than its own architecture. PCIe is backward compatible with PCI, meaning that PCI software can still detect and work with PCIe, but it won’t be able to use all features of PCIe.
The available bandwith of PCIe card is not only dictated by the PCIe slot length. Version is another parameter that affects PCIe card’s bandwith. There are four versions (generations) of PCIe.
	Version 1	Version 2	Version 3	Version 4
Bandwith in each direction, per lane	250 MB/s	500 MB/s	984.6 MB/s	1969.2 MB/s

As you can see by looking at the table 2, the available bandwith of PCIe card is almost doubled with each version. For example, the available bandwith of x16 card with PCIe version 1 equals to x4 card with PCIe version 3. If the PCIe card is going to be attached to the PCI slot with different version, then the available bandwith will be identified by the lowest version between card and slot. PCIe also includes features like Quality of Service (QoS), hot plug & hot swap support, advanced power management.
 Memory read request from the CPU targeting specific Endpoint Though a PCIexp
The figure below graphically illustrates a memory read request from a CPU targeting a specific endpoint. The Root Complex, on behalf of a processor starts the non-posted memory read transaction by creating the MRd (Memory read request) packet. Amongst other information, this packet contains a requester ID (which is Root Complex in this case), targeted address, packet type and length of transfer (doublewords). The root complex sends this packet to the switch‘s upstream port (the port which points to the root complex). The switch can be logically represented as three PCI-to-PCI bridges connected to each other via internal bus as shown in the below, showing the case of the switch having five PCI-to-PCI bridges. Each bridge contains memory, address limits and I/O base registers. Switch A decodes the MRd packet and compares its values with base/limit addresses ranges of two bridges with downstream ports. When Switch A finds the right port, it forwards the packet to that port, such as Switch B. Switch B performs a similarly routine to find the right port.

When the endpoint receives the MRd, it will accept this packet and create completion packet (CpID). CpID also includes requester ID (bus#, device#, function #) in its overhead (which was copied from MRd) so that this packet could be routed back to the Root Complex. When CpID arrives to switch B, the switch is routing the packet based on the bus number of requester ID. When CpID is received by switch A from switch B, it routes the packet similarly. Finally, when Root Complex receives the CpID, it compares the value of receiver ID field in CpID’s overhead with its own ID. If ID is correct and CpID has no errors, then it is forwarded to processor.

PCIe is a layered protocol. It consists of software, physical, data link and transaction layers.
Transaction layer
The transaction layer packet (TLP) originates at TLP. Transaction layer has virtual channels buffers (VC) that hold TLP arrived from software or link layers. One of the main functions of Transaction layer is Flow control, which ensures that the transmitter will not overload these buffers with TLPs . Flow control is based on credit scheme, meaning that transmitter will only send TLP when the receiver’s buffer has enough space to store it. This layer is also responsible for QoS protocol.
Data link layer
The data link layer ensures the data integrity of the packets that are sent or received by two adjacent devices. It also checks the LCRC values and the sequencing of the packets. The data link layer generates three important types of data link layer packets (DLLP) – acknowledge or no acknowledge (ACK/NAK), flow control (FCx) and power management (PMx). When the transmitter sends the TLP packet, it must be sure that this packet reached the receiver without any problems. Before transmitting any packet, the transmitter copies the TLP into a special buffer named the replay buffer (or Retry Buffer). If the packet is lost during transmission or reached the receiver in “corrupted” state, the receiver must inform transmitter to resend the packet. ACK/NAK protocol is used to acknowledge the transmitter about the packet arrival. If the packet arrived, then receiver sends ACK message to inform transmitter that everything is OK. After receiving ACK message, transmitter can remove TLP from the replay buffer. The receiver sends NAK when the TLP packet has a wrong CRC (LCRC) value. If transmitter has received NAK 4 times and replayed the TLP 3 times, then it logs error and retrains the link. If transmitter hasn’t received any ACK messages or received NAK message, then transmitter must resend the TLP and all other packets that were sent after it. This method resolves the problem of DLLPs not being acknowledged. For example, the transmitter was acknowledged with ACK, but this DLLP has a bad CRC value. The transmitter will not acknowledge receiver about this problem and will resend the TLP packet again.
What if Replay Buffer gets overloaded because transmitter doesn’t receive ACK from the receiver fast enough? Thankfully there is a time period in which the receiver must answer the transmitter about the received packet. This technique prevents the replay buffer from getting overloaded over a short period of time and helps calculate the appropriate size of a replay buffer. Sure it would be more convenient to have a replay buffer with a huge memory so there couldn’t be any overload problems, but this will make the price of PCIe device very big, which is not an appealing thing for a buyer.
Physical Layer
Physical layer describes the electrical characteristics of PCIe. This layer generates ordered sets (PLP) which is used for linking management and is exchanged between the physical layers between transmitters and receivers. The transmission unit of physical layer is called a lane and consists of two pairs of wires, one of which is for transmitting and another one is for receiving data. PCIe devices communicate with each other in full-duplex mode, meaning that they can receive and send data at the same time. So why do we need two wires for each direction? This is because of the technique called Differential Signaling. To understand this technique, we should mention Single Ended Signaling that was used in PCI:

Figure 10 illustrates that in the case of Single Ended Signaling, there is only one wire used to send the signal and the receiver reads the signal as 1 if it is supplied with 5V. In the case of differential signaling, the second wire is used to send a “mirrored” signal (inverted polarity). The receiver identifies 0 or 1 by finding the difference between the volt of blue and black line. If the difference between the volt of blue and black line is higher than a certain value, then it is signified as a 0; if the difference is lower, the result is 1. The Differential Signaling technique is better because it is faster to adjust the voltage if we need different value (from 0 to 1 or from 1 to 0). The other reason is that it has more immunity to noise. The illustration below illustrates this condition. When noise occurs, both of the wires are going to get affected by it. So no matter if the noise occurred in the bus or not, the volt difference between the two signals is always going to be the same.
PCIe addressing and routing
When a device receives a packet at an ingress port, it first checks this packet for errors and then decides whether: 1) Accept the packet; 2) Forward the packet to other egress port (if it has them); 3) Reject the packet. Receivers check the incoming type of packet to determine whether to forward this packet. If the packet type is DLLP or PLP, it is not going to be forwarded through other ports of the receiver. These packets do not contain any routing information in their headers and solely intended for link management between two adjacent devices. TLP is the only type of packet that is going to be forwarded and it contains routing information in its header. Devices that contain multiple ports (e.g. Switch, Root Complex) are intended to perform routing function on the packets. Endpoints are limited in their routing capabilities, which means that they can only accept or reject TLPs. Before devices can accept, forward or reject data, they must be configured to do so. Using plug and play, they first must be discovered. Then they are assigned with memory and I/O address resources and programmed with routing.
PCIe TLP routing basics
TLP uses four address spaces: memory, I/O, configuration and messaging. Memory address space is used to address system memory or I/O memory. I/O address space is used to address legacy PCI devices. Configuration address space is used to address register of a specific I/O device. Message address space is used for control signals.
Split transaction technique is used when transmitter sends non-posted request packet. It awaits for a completion packet from the receiver. This means that two separate transactions will be used to send the request and completion packets at different times. The receiver will send a completion packet only after it finds the requested data and is ready to send packets. This is much better than old technique used by PCI bus, which required two devices to seize the whole bus for transaction. This resulted in big delays because of busyness of the bus and packet retransmission in case of an error.
TLPs can be routed using address routing, ID routing and implicit routing. Memory and I/O transactions are routed using address routing. ID routing is used to find the logical location of registers within PCI compatible bus (IDs consist of the bus, device and function numbers). Implicit routing is used when a packet needs to reach a device which is known and has fixed position (e.g. Root Complex).
TLP consists of 3 or 4 DoubleWords which are 12 and 16 bytes long respectively. Type fields identify which routing is going to be used with this packet. This chart illustrates the header structure of TLP:

When TLP is received at the ingress port, checks are made first by the physical and data links layers for errors. If there are no errors the transaction layer starts to be examined. The first double word is looked at in the TLP. Then it will check if the TLP arrived its intended recipient or not. If yes, it will be accepted. If it is not the intended recipient, and it is a device with multiple ports, then the TLP will be forwarded to the respective egress port. If this is not intended recipient and is not the device which is located on the way to the recipient, then the packet will be rejected.
Address Routing
Address routing is used to route TLPs destined to or originating from memory, direct mapped I/O and I/O devices. The address range In TLP’s overhead can be 32 bits using 3DW or 64 bits using 4DW. Legacy I/O devices cannot be addressed with 64-bit addresses.
When an endpoint receives TLP indicating the address routing in the Type field, it simply compares the address in TLP’s overhead with its BAR (Base Address Register). BAR is a register which keeps the device’s address. If two compared addresses are equal, then endpoint accepts the packet. Otherwise it is going to reject it.
When a switch receives TLP indicating the address routing in the type field, it first resolves if the switch is the intended recipient. If not, it compares the address in TLP’s overhead with Base and Limit registers of each PCI-to-PCI bridge (with egress ports). Base and Limit registers identify the range of addresses located through the specific port. For example, If Base register has value 100 and limit register has value 200, it means that devices with addresses 100-200 are located through this port. Upstream TLPs are always routed through the upstream port if they do not match the base and limit registers and are not intended for this switch.

ID Routing
In ID routing the devices route the TLPs using ID (bus + device + function numbers) numbers. This addressing was used in PCI and PCI-X topology. ID routing is also used with completion and message packets. There are limits on bus, device and function numbers. PCIe topology can consist of maximum 256 buses, 32 devices on each bus and 8 functions on each device.
When an endpoint receives TLP with type indicating ID routing, it compares its bus, device and function numbers with ID number of TLP’s overhead. If comparing values are equal, then the device accepts the TLP. Otherwise, it will reject the packet.
Similar to endpoints, switches first compares its bus, device and function numbers with ID number of TLP’s overhead. If comparing values are equal, then the device accepts the TLP. If not, the switch starts to compare the bus number value of TLP’s overhead with range of secondary-subordinate registers of each PCI-to-PCI bridges. Secondary register contains the bus number that is directly attached to the downstream port. Subordinate register contains farthest & largest bus number of downstream device located through the downstream port. Upstream TLPs are always routed through the upstream port if they do not match the range of secondary-subordinate registers and are not intended for this switch.

Figure 14
Implicit Routing
Implicit routing is used when there is a need to inform the device with known and fixed position (such as Root Complex) about power, error, interrupt management problems. Implicit routing can be used only with message TLPs. Message TLPs can also be routed using address or ID routing. First 3 bits of the type field (which is 5 bits long) identify the type of routing and where this packet should be sent. Table 3 shows all cases. The last 2 bits of the type field identify whether or not this is a message TLP. Message TLP can also be sent as a broadcast packets from root complex.
When an endpoint receives the message TLP, it will check the first 3 bits to figure out the routing type and if this packet is appropriate for it. For example, it won’t receive the message that was intended for Root Complex.
Similar to the endpoint, a switch will check the first 3 bits to figure out the routing type and if this packet is appropriate for it. For example, if a switch receives broadcast message TLP on its uplink port, it will spread this packet through all downstream ports. It won’t accept broadcast message that will be received through the downstream port. Another example is that the switch won’t accept the implicitly indicated message pointing to the Root Complex if this message was received at uplink port.

References:
http://www.lintech.org/comp-per/01buses__ver2_.pdf
http://en.wikipedia.org/wiki/System_bus
http://www.mathcs.emory.edu/~cheung/Courses/355/Syllabus/5-bus/asynch-bus.html
http://en.wikipedia.org/wiki/PCI_Express
http://www.hardwaresecrets.com/article/Everything-You-Need-to-Know-About-the-PCI-Express/190/2 - Gabriel Torres, 2012
http://www.mindshare.com/files/resources/mindshare_pcie_replay_buffer_sizing.pdf - Joe Winkles, 2003
http://www.plxtech.com/files/pdf/technical/expresslane/TechnologyBrief_PCIExpress_Q4-2003.pdf
http://pciexpress-datalinklayer.blogspot.com/ - 2008
http://www.icverification.com/BusProtocols/PCIE.php